MODEL YEAR(S)
CORVETTE 1994 -1996
KEY T-HARNESS IMMOBILIZER
N/A N/A GM's VATS ANTI-THEFT System, Ignition Key has Chip, Requires 791 Bypass Module
PART COLOR LOCATION
12 VOLT CONSTANT RED (+) IGNITION SWITCH HARNESS
STARTER YELLOW (+) IGNITION SWITCH HARNESS
STARTER 2 N/A
IGNITION 1 PINK (+) IGNITION SWITCH HARNESS
IGNITION 2 N/A
IGNITION 3 N/A
ACCESSORY/HEATER BLOWER 1 ORANGE (+) IGNITION SWITCH HARNESS
ACCESSORY/HEATER BLOWER 2 N/A
KEYSENSE N/A
PARKING LIGHTS ( - ) N/A
PARKING LIGHTS ( + ) BROWN (+) @ HEADLIGHT SWITCH
POWER LOCK RED/BLACK (TYPE C) See NOTE *2 IN EITHER KICK PANEL
POWER UNLOCK ORANGE/BLACK (TYPE C) See NOTE *2 IN EITHER KICK PANEL
DOOR TRIGGER BLACK/WHITE (-) and GRAY/BLACK (-) Use both, See NOTE *3 IN EACH KICK PANEL
DOMELIGHT SUPERVISION BLACK/WHITE (-), Requires #775 Relay IN DRIVERS KICK PANEL
TRUNK RELEASE LIGHT BLUE (-), Requires #775 Relay @ HATCH RELEASE SWITCH
SLIDING POWER DOOR N/A
HORN BLACK (-) @ STEERING COLUMN HARNESS
TACH RED/BLACK @ ECM, above the BATTERY
WAIT TO START LIGHT N/A
BRAKE WHITE (+) or LIGHT BLUE (+) @ SWITCH ABOVE BRAKE PEDAL
FACTORY ALARM DISARM GREEN (-) IN EITHER KICK PANEL
ANTI-THEFT See NOTE *1 GM's VATS System @ Ignition Switch
EXTRA INFORMATION
NOTE *1 The VATS (Vehicle Anti-Theft System) wire may be (2) thin YELLOW wires, (2) thin TAN wires or (2) thin WHITE wires, these wires are usually in a ORANGE or BLACK HEAT SHRINK TUBE, but at times are left out of the tube and ran by themselves up under the dash to the Security Module under the Dash.
NOTE *2 This is a TYPE "C" DOOR LOCKING SYSTEM, the PASSENGER switch is the MASTER switch for testing.
NOTE *3 The BLACK/WHITE (-) is for the DRIVERS DOOR and the GREY/BLACK (-) is for the PASSENGER DOOR, use both and DIODE ISOLATE when connecting to an ALARM SYSTEM.